## Slide 1: Chapter 15 Broadband Home Networks
*
Chapter 15 Broadband Home Networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: Chapter 14

## Slide 2: Objectives
*
Network Management: Principles and Practice
© Mani Subramanian 2010
  Broadband home networks overview
  Applications and application protocols
  Middleware between applications and transports
  Transport technologies
  Wired home networks
    Comprehensive view
    Lower layer protocols
    Ethernet-like protocols and management
    Power Ethernet
  Wireless home network
    WiFi (802.11a/b/g) wireless LAN
    802.11 standards and amendments
    Hierarchical network using access point
    Basic service set (BSS)
    MAC protocols: DCF, PCF, and hybrid
  Special network management considerations
    Security management
    QoS management
    Centralized management
    WLAN MIBs
Chapter 15 Broadband Home Networks

## Slide 3: Home Networking Technologies
*
Middleware and higher layer protocol networks
  HAVi (Home Audio-Video interoperability)
  Jini (Java-based middleware/network)
  UPnP (Universal Plug and Play)
  OSGi (Open Service Gateway initiative)
Lower Layer wired protocol based networks
  IEEE 802.3 Ethernet
  VHN (Versatile Home Network)
  IEEE 1394 (FireWire)
  Cable
  HomePNA (Home Phoneline Network Alliance)
  HomePlug (Power Line Communication, PLC)
Wireless LANs (Local Area Networks)
  IEEE 802.11 WLAN
  HomeRF
Wireless PANs (Personal Area Networks)
  IEEE 802.15.1 Bluetooth
  IEEE 802.15.3a UWB (Ultra Wideband)
  IEEE 802.15.4 Low data rate PAN
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 4: Networking Protocols
*
  Notes
Two Groups
  Physical interconnects
    X-10
    CEBus (Consumer Electronics Bus)
    IrDA (Infrared Data Association)
    HomePlug
    HomePNA
    WiFi 802.11
    Bluetooth
    Ethernet
    IEEE 1394
    USB (Universal Serial Bus)
  Service or application middleware
    HAVi (Home Audio/Video interoperability)
    UPnP (Universal Plug and Play)
    Jini
    OSGi (Open Services Gateway initiative)
Chapter 15 Broadband Home Networks
Network Management: Principles and Practice
© Mani Subramanian 2010

## Slide 5: Application Layer Protocols
*
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 6: Home Network Protocol Architecture
*
  Notes
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks
Figure 15.1 Home Network Protocol Architecture

## Slide 7: Home Networks
*
  Notes
Three access networks and modems
Four types of distribution networks
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 8: HAVi Protocol Architecture
*
  Notes
Application for home entertainment and AV devices
HAVi Components
  Device
    FAV (Full Audio Visual)
    Intermediate AV
    Base AV
    Legacy AV
  Device control module (DCM): Aggregate of FCMs
  Functional control module (FCM): Controls application functions
Peer-to-peer environment
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 9: HAVi Communication
*
  Notes
  Lower layer: IEEE 1394
    Function control protocol: IEC 61883.1
    Device control protocol: IEEE 1212
    HAVi messages
  Services
    Discovery Messaging
    Lookup Events
    Configuration Reservation
    Device control User interaction
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 10: Jini Middleware
*
Components
  Device – Java object / Client
  Access: RMI (Remote Method Invocation)
  Services
    Lookup
    Discovery
Based on Java platform
Distributed environment for devices to communicate; Not housed in a single computer
Forms impromptu communities – Group of shared services
Federation: Jini communities linked together
Jini surrogate host to handle non-Jini host
JiniME (Mobile Edition) for mobile devices
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks
  Notes

## Slide 11: Jini Network: Service
*
  Notes
Lookup Service:
  Client requests service (e.g., clock)
  Lookup service: locator
  Service provides the service (e.g., TV)
Network: Any network supporting Jini service
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 12: UPnP Protocol Architecture
*
  Notes
Universal plug and play
Active addition and deletion of devices
Components
  Devices
  Services
  Control points
Peer-to-peer network
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 13: UPnP Network
*
  Notes
Underlying networks with standard protocols:
  HomePlug
  IEEE 1394
  LAN
  WLAN
Gateway and cable modem link to Internet
Dynamic configuration of devices offering services requested by control points
Needs zero-configuration
Automatic discovery of devices
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 14: OSGi Gateway
*
  Notes
OSGi: Open Service Gateway initiative
Platform for residential gateway
Specifies API only, not underlying implementation; Platform and application independent
Service and device discovery functions
Imports multiple discovery protocols and registers them as OSGi services
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 15: OSGi Home Network Architecture
*
  Notes
Residential OSGi Gateway
External link to Internet via embedded modem with interface to cable, DSL, or wireless access network
Intra-home networks with multiple protocols integrated with OSGi
Jini creates impromptu communities automatically
IEEE 1394 network for AV devices
IEEE 802.11 and Ethernet networks for mobile fixed data devices
Imports discovery services from other protocol networks
Source: Dobrev, et.al., IEEE Communications Magazine, Aug. 2002
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 16: Lower Layer Networking Protocols
*
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 17: Lower Layer Protocols for Networked Appliances
*
  Notes
Category | Appliance | Protocol
Home Automation and Control | Lighting, Appliances, Climate Control | EIB, LonWorks, X10, CEBus
Entertainment | A/V Equipment, TV, PC | IEEE 1394
Communications | Telephone, Cell Phone, Intercom | IEEE 1394, HomePNA
Computers and Information | PC, Peripherals, PDA | Ethernet, WiFi
Issues:
  rt, near-rt, and non-rt, requirements
  Multiplicity of component networks
  Backbone QoS
  Interoperability
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 18: IEEE 1394
*
  Notes
Wired IEEE 1394
  Applicable to audio, video, and high-speed data
  Transport speed 100, 200, and 400 Mbps
  1394b: 800 and 1600 Mbps
  Extension to 3.2 Gbps in the future specifications
  Supports asynchronous and isochronous
  Flexible topology; supports daisy chaining and node branching
  Active connect and disconnect
Wireless /1394 bridge
Source: Nakagawa, et. al.
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 19: USB
*
  Notes
Universal Serial Bus (USB)
  Alternative to Ethernet as a computer peripheral interface
  Data-centric, not multimedia-oriented
Source: Nakagawa, et. al.
USB 1.0 1.5 Mbps Low speed Cable length = 3m
USB 1.1 12 Mbps Full Speed Cable length = 3m
USB 2.0 400 Mbps High speed Cable length = 5m
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 20: Residential Ethernet
*
  Notes
Medium
  UTP-CAT5 (Unshielded twisted Pair Category 5); Maximum 100 meters
  Optical Fiber in new homes
Requirements different from enterprise Ethernet
  Multiplicity of multimedia and networked appliances
  Single physical port, multiple logical / channel interface handled by ifStackTable (RFC 2863)
  ifOctets redefined to handle 10 Gbps
  IP phones wired with powered Ethernet cable
  New MIB for powered Ethernet
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 21: Power Ethernet MIB
*
  Notes
pse: Power sourcing equipment
pethObjects has three groups:
  pethPsePortTable: MOs for status of PSE device ports
  pethMainPseObjects: MOs for PSE device
  pethNotificationControlTable: Notifications
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 22: IEEE 802.11 Wireless LAN
*
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 23: 802.11 PHY & MAC
*
  Notes
MAC Layer
  CSMA/CA (CSMA/ Collision Avoidance) is used: (CSMA/CD in 802.3)
  BSS Basic service set comprise AP (Access Point) and STAs (Stations); a.k.a. Wi-Fi
  Choice of coordination function by AP
    DCF Distributed coordination function
      Asynchronous
      Contention-based
    PCF Point coordination function (optional)
      Synchronous
      Contention-free
PHY Layer
  802.11b @ 2.4 GHz & data rate 11 Mbps
  802.11a @ 5 GHz & data rate 54 Mbps
  802.11g extends 802.11b to 54 Mbps with OFDM
IBSS: Independent BSS
  Ad-hoc configuration of 802.11
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 24: 802.11 Standards & Amendments
*
802.11a | 54 Mbps data rate 5.15 MHz to 5.35 and 5.4 MHz to 5.825 MHz
802.11b | 11 Mbps data rate at 2.4 GHz
802.11e | Addresses QoS issues
802.11f | Addresses multivendor AP interoperability
802.11g | Higher data rate extension to 54 Mbps in the 2.4 GHz
802.11h | Dynamic frequency selection and transmit power control for operation of 5 GHz products
802.11i | Addresses enhanced security issues
802.11j | Addresses channelization in Japan’s 4.9 GHz band
802.11k | Enables medium and network resources more efficiently
802.11v | Wireless network management (in preparation)
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks
  Notes
Table 15.1 IEEE 802.11 Standards and Amendments

## Slide 25: Residential WLAN
PC
Kitchen
Family room
Dining Room
Bedroom
Den
Kitchen
Touch Pad
MP3 Player
WebPad
AP
Internet
Chapter 15 Broadband Home Networks
Figure 15.4 Residential WLAN
Network Management: Principles and Practice
© Mani Subramanian 2010
*

## Slide 26: WiFI Network Infrastructure
Chapter 15 Broadband Home Networks
*
Internet
Layer 2/3
Switch
802.11
802.3
IP
Layer 2/3 bridge is traditional Ethernet hub
AP performs security functions
AP
User
  Notes
Figure 15.5 WiFI Network Infrastructure
Network Management: Principles and Practice
© Mani Subramanian 2010

## Slide 27: Enterprise WLAN
*
  Notes
An access point (AP) and multiple stations (STAs)
AP works as a bridge
Every transmission is between AP and STA(s)
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks
Figure 15.6 Enterprise WLAN

## Slide 28: Evolution of WLAN Security
*
  Notes
WEP Wired Equivalent Privacy
WPA WiFi Protected Access – IEEE 802.11i based
WPA2 802.11i (?)
Source: Network World 2003
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 29: Security Management
*
  Notes
Evolution:
WAP (Wireless Application Protocol) Security
  WAP Wireless transport layer security (WTLS)
    Based on transport layer security (TLS) or secured sockets shell (SSL)
    “Walled garden” “vertical” integrated approach
WEP Wired Equivalent Privacy
WPA WiFi Protected Access
WPA2 WPA with IEEE 802.11i
3G network security
  3GPP (Third Generation Partnership Project) and 3GPP2 plan for IP to wireless device
  Open standard SNMP-based
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 30: WLAN Broadband QoS Issues
*
  Notes
Broadband comprises:
  Voice: Real-time data
  Video: Streaming data with/without delay
  Data: Non-real time data
Broadband QoS determined by MAC and PHY layers
QoS Parameters:
  Datarate
  Delay bound
  Jitter
Two types of media access (MAC)
  DCF (Distributed Control Function): CSMA/CA
  PCF (Point Control Function): Polled Xmission
Both DCF and PCF fail to satisfy broadband service
Range dependencies
  Power level
  Antenna choice
    Diversity antenna focuses beam
    Diversity reception improves S/N ratio
    MIMO (Multiple Input Multiple Output) technology enhances reception
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 31: IEEE 802.11e QoS Table
*
  Notes
UP (user priority) | AC (access category) | Service type
2 | 0 | Best Effort
1 | 0 | Best Effort
0 | 0 | Best Effort
3 | 1 | Video Probe
4 | 2 | Video
5 | 2 | Video
6 | 3 | Voice
7 | 3 | Voice
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks
Table 15.2 IEEE 802.11e QoS Table

## Slide 32: 802.11 MIB
*
  Notes
Entity | OID | Description
dot11smt | ieee802dot11 1 | Station management attributes: WEP security, power, transmission
dot11mac | ieee802dot11 2 | Mac attributes
dot11res | ieee802dot11 3 | Resource type attributes
dot11phy | ieee802dot11 4 | Physical attributes
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 33: Centralized Management of WLANs
*
  Notes
CAPWAP interoperable protocol standard
Centralized Access Controller manages multiple BSSs via Wireless Termination Points (WTPs)
CAPWAP – IETF compatibility achieved by one- to-one relationship between ifIndex and WTP ID + Radio ID
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks
Figure 15.9 Centralized Management of WLANs

## Slide 34: CAPWAP Base MIB
*
  Notes
CAPWAP MIB in proposal stage
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 35: CAPWAP Base MIB
*
Entity | OID | Description
capwapBaseObjects | capwapBaseMIB 1 | CAPWAP MIB objects
capwapBaseAc | capwapBaseObjects 1 | Access Controller Objects group
capwapBaseAc NameListTable | capwapBaseAc 9 | Objects that display AC name list
capwapBaseMac AclTable | capwapBaseAc 10 | Set of objects that configure station ACL
capwapBaseWtps | capwapBaseObjects 2 | Wireless Termination Point Objects group
capwapBaseWtp StateTable | capwapBaseWtps 1 | Objects that display WTP CAPWAP FSM state
capwapBaseWtp Table | capwapBaseWtps 2 | Objects that display and control WTPs in running state
capwapBaseRadio BindTable | capwapBaseWtps 3 | Objects that display mapping relationship between specific interface of 'WTP Virtual Radio Interface' ifType and PHY radio
capwapBaseStation Table | capwapBaseWtps 4 | Objects that display stations which are accessing the wireless service provided by the AC
capwapBaseWtpRebootStatsTable | capwapBaseWtps 5 | Objects that display WTPs' reboot statistics
capwapBaseRadioStatsTable | capwapBaseWtps 6 | Objects that display statistics on radio’s behavior, and reasons why the WTP radio has been reset.
capwapBaseParameters | capwapBaseObjects 3 | CAPWAP Base Parameters group
capwapBaseStats | capwapBaseObjects 4 | CAPWAP Statistics group
capwapBaseNotifyVar Objects | capwapBaseObjects 5 | Objects used only in notifications
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 36: IEEE 802.15 WPANs (Wireless Personal Area Networks)
*
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 37: WPANs
*
  Notes
802.15.1 Bluetooth base line standard
802.15.2 Coexistence of 802 wireless technologies
802.15.3 High-rate radio (>20 Mbps)
802.15.4 Low-rate radio (<200 kbps)
Source: Callaway, et. al., IEEE Communications Magazine, Aug. 2002
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks

## Slide 38: Bluetooth Protocol Stack
*
  Notes
Short range up to 10m
2.042 GHz to 2.483 GHz band
79 channels of 1 MHz width
Data rate 1 Mbps
Time division multiplexing
Master-slave architecture
Voice support synchronous connection-oriented link
Data support using asynchronous connectionless link
Source: Bisdikian, IEEE Communications Magazine, Dec. 2001
Network Management: Principles and Practice
© Mani Subramanian 2010
Chapter 15 Broadband Home Networks