## Slide 1: Chapter Highlights
Nature of sound
  Sine waves, amplitude, frequency
Traditional sound reproduction
Digital sound
  Sampled
  Synthesized
Advantages of digital sound
Guidelines for digital sound in multimedia.
CHAPTER SEVEN
SOUND

## Slide 2: Nature Of Sound
Sound is a form of mechanical energy transmitted as vibrations in a medium.
Sine wave captures three features of sound:
  Amplitude
    Perceived as volume.
  Frequency
    Perceived as pitch.
  Duration
    Length of time sound lasts.

## Slide 3: Traditional Sound Reproduction
Analog sound capture.
    Sound waves vibrated diaphragms of early microphones.
    Vibration caused a stylus to inscribe a continuous pattern on tinfoil or on a wax cylinder.
Reproduce the analog sound.
    Rotate a drum while in contact with a stylus
    Movements of stylus are electrically amplified to vibrate the drum of a speaker
    Changes in air pressure produced the sound.
High-fidelity analog sound is still the final output stage for digital audio.

## Slide 4: Digital Sound
  Represented As Discrete Elements Of Information

## Slide 5: Digital Sound
Two major types of digital sound:
  Sampled sound: digital recording of previously existing analog sound wave.
    File contains numeric values to describe the amplitude of the sound wave at a particular instant.
    Used to capture and edit naturally-occurring sounds.
    Synthesized sound: new sound generated by the computer.
    File contains instructions the computer uses to reproduce the sound.
    Used to:
    Create original compositions
      Produce novel sound effects.

## Slide 6: Sampled Sound
Analog to Digital Converter captures separate measures of sound amplitude.
  Samples are recorded as digital numbers.
Digital values are used to recreate the analog form using a Digital to Analog Converter.
Quality of the sampling depends on:
  Sample resolution
  Sample rate.

## Slide 7: Sample Resolution
Number of bits to encode amplitude.
  Sample resolutions range from 8-bit to 24-bit.
8-bit resolution captures 256 different amplitude levels.
  Adequate for limited decibel range.
16-bit CD quality sound has 65,000 different levels.
24-bit DVD audio can generate over 16 million different levels.

## Slide 8: Sampled Sound Distortions
Quantization: rounding a sample to the closest available value in the code being used.
  May produce background hissing or grainy sound.
  Caused by low sample resolution
  Solution: record at higher resolution
    Use 16-bit rather than 8-bit to increase the range of amplitudes.

## Slide 9: Sampled Sound Distortions
Clipping: wave amplitude exceeds available sample values.
  Causes:
    Recording equipment isn't designed for selected decibel range or
    Mixing tracks with amplitudes that exceed the available range.
  Result is harsh, distorted sound.
  Solutions:
    Lower amplitude of source sound within the limits of the ADC circuitry.
    Adjust volume of mixed tracks or use higher sample resolution.

## Slide 10: Sample Rate
Number of samples taken in a fixed interval of time.
  Stated in thousands of Hertz, or kilohertz.
  Determines the range of frequencies that can be represented in a digital recording.
Two measurements capture each cycle of the sound wave:
    High value or peak
    Low value or trough.
  CD-quality sound captures 44.1kHz to record frequencies as high as 22.05kHz.
Highest frequency the human ear can detect is 20kHz.

## Slide 11: Sample Rate Distortion
Aliasing: false representation of high frequencies as low frequencies.
  Occurs when source frequency is greater than one-half the sample rate being used.
  Solutions:
  Apply filters to source sound to eliminate frequencies above the sample rate.
    Oversample the source sound:
      Use digital filters to eliminate the high frequencies.
      Then downsample to reduce the sample rate in the audio file.

## Slide 12: Sound File Size
Sound files are large.
  60 seconds of stereo CD quality sound = 10 MB.
Reduce file size and maintain quality:
  Select sample rate and resolution to match the sound type.
    Human speech can accurately be captured at 11.025kHz with 8-bit resolution and have a smaller file.
  Lower sample rate and resolution to reduce file size.
Stereo file size = sample rate * sample size (in bytes) * sample time (in seconds) * 2 (stereo)

## Slide 13: Sound Compression
Compression is best strategy to lower file size for sounds with wide range of frequencies and amplitudes.
Lossy codecs use various techniques to reduce sound file sizes.
  Psychoacoustics: eliminates frequencies indistinguishable to the human ear.
  Variable bitrate encoding (VBR): alters the number of bits to encode the sample depending on the complexity of the sound.
Notes: Compression strategies are both lossless and lossy. Have students comment on why lossless strategy is not used in sound, but is critical for text compression.

## Slide 14: Sampled Sound File Formats
AIFF: Apple Computer
  Uncompressed, high quality sound.
WAV: Microsoft and IBM standard
  Uncompressed, high quality sound.
AU: Sun Microsystems
  Internet transmission of lower quality sound files.
RealAudio: Real Media
  Streaming audio at low bandwidths.
MP3: (MPEG-1, audio layer 3)
  Significant compression of high quality sound.
WMA: Windows Media Audio
  Delivers lossy compression comparable to MP3 at lower bitrates.
AAC: Advanced Audio Coding
  Successor to MP3 specified in the MPEG-4 standard.
  Produces better quality sound than MP3 standard at comparable bitrates.
AIFF: أبل كمبيوتر غير مضغوط ، صوت عالي الجودة.
WAV: مايكروسوفت ومستوى IBM غير مضغوط ، صوت عالي الجودة.
الاتحاد الافريقي: صن مايكروسيستمز
نقل الإنترنت لملفات الصوت منخفضة الجودة.
الصوت الحقيقي: وسائل الإعلام الحقيقية
تدفق الصوت عند عرض النطاق الترددي المنخفض.
MP3: (MPEG-1 ، طبقة الصوت 3)ضغط كبير من جودة صوت عالية.
WMA: ويندوز ميديا أغنية :توفر ضغطًا ضارًا مقارنةً بملفات MP3 عند معدل
البت المنخفض.
AAC: أغنية ترقيمها المتقدملخلف إلى MP3 المحدد في معيار MPEG-4.
ينتج صوتًا أفضل جودة من معيار MP3 في معدلات البت المماثلة

## Slide 15: Synthesized Sound
Computer sends commands to specialized electronic device called a synthesizer.
MIDI (Musical Instrument Digital Interface).
  Most common standard to code commands for synthesizers.
  Codes provided for:
    Specific instruments
    Notes
    Force and duration of note
    Routing commands to different instrument channels
    Specialized control functions.

## Slide 16: MIDI
Messages (or commands) can be sent to any one of 16 channels.
  Voices or instruments are assigned to a channel.
  Multitimbral systems can play multiple instruments by simultaneously processing commands in different channels.
  Polyphonic systems play more than one note at once.

## Slide 17: MIDI Sound System
Simplest system contains: مهههههم
  Digital musical instrument to create messages
  Sound synthesizer to interpret the messages
  Amplifier/speaker output system.
Sequencer
  Device to control the flow or sequencing of the MIDI data to a multitimbral synthesizer.
  المنظم
  جهاز للتحكم في تدفق أو تسلسل بيانات MIDI إلى مُركِّب multitimbral.

## Slide 18: MIDI On A Computer
Software and hardware emulate the MIDI sound system.
Hardware
  Soundcards include synthesizers.
  Interface ports for MIDI-input devices.
Software
  Sequencer software can place notes on a musical scale.
  Editing includes changing pitch, tempo, duration and volume of notes, arrangement and timing of instruments.

## Slide 19: SAMPLED Vs. Synthesized
Advantages Sampled | Advantages Synthesized
1. High quality. | 1. Exceptional editing control.
2. Ease of creation. | 2. Small file size.
3. Ease of editing. | 
4. Consistent playback quality. | 
Challenges Sampled | Challenges Synthesized
1. Large file sizes. | 1. Musical expertise required.
2. Editing limitations. | 2. Playback quality is not consistent.
 | 3. Not effective for natural sounds and human voice.

## Slide 20: Advantages Of Digital Sound
Noise reduction
Recording accuracy
No generation decay
Durability
Random access
Editing is easier and less expensive
Easily distributed by:
  CDs
  Networks.

## Slide 21: SOUND and the INTERNET
  Increased Bandwidth + Standard File Formats + Simplified User Access = Sound On The Web.

## Slide 22: Delivering Digital Sounds
Downloaded audio transfers the complete audio file from the server to the client.
  File remains on client computer for replay and editing.
Progressive downloads: file is saved to client computer, but begins to play from RAM as it is downloading.
Streaming audio: real-time sound that is played as it is being delivered. Not saved on client computer.
  Requires special protocols, special servers, special media formats and players.
Notes: Discuss benefits and drawbacks of each technique. Note particularly the copyright issues with each. Have students identify methods used by iTunes, a live concern of a band, a song shared on peer to peer networking.

## Slide 23: Guidelines For Use Of Sound
Identify the purpose of the sound and use it for good reasons.
Use high-quality sound.
Conserve file space.
Consider playback environment.
Avoid excessive use of sound.
Organize sound files and preserve original sources.

## Slide 24: WRAP UP
Two approaches to creating digital sound.
Sampled sound depends on:
  Sample resolution and Sample rate.
  Distortions degrade sampled sound.
Synthesized sound depends on:
  Synthesizer and Musical knowledge.
  Distortions come from poor sound output hardware.
Advantages and challenges of each.
Advantages and guidelines for digital sound.
Distributing sound on the Internet.